## Slide 1: Photogrammetry
Raju Shrestha
Roll No. 48/2079
July 29, 2024

## Slide 2: Contents
Photogrammetry and it’s applications
Orientation and Triangulation
Stereo Model Compilation
Stereoscopic 3D Viewing
Stereoscopic Measurement

## Slide 3: Photogrammetry
Photogrammetry is the science of obtaining reliable information about physical objects and the environment without physical contact with the objects.
This involves the process of recording, measuring and interpreting photographic images and patterns of electromagnetic radiant imagery.
In short, Photogrammetry is the science of making measurements from photographs, especially for creating maps from aerial photographs.

## Slide 4: Photogrammetry
Photogrammetry can be categorized based on different criteria, such as:
    Platform used for capturing images
    Type of images used, and
    Application area.
Aerial Photogrammetry: Involves taking photographs from an airborne platform, such as an airplane or drone.
  Used for mapping large areas, creating topographic maps, urban planning, agriculture, forestry, and environmental monitoring.
  Covers large areas, requires high-altitude platforms, and typically uses vertical images.

## Slide 5: Photogrammetry
Terrestrial (Close-Range) Photogrammetry: Involves taking photographs from ground-based platforms, such as tripods or handheld cameras.
  Used for documenting buildings, historical sites, forensic analysis, architecture, engineering, and construction.
  Suitable for smaller areas and objects, provides high detail and accuracy for close-up subjects.

## Slide 6: Photogrammetry
Satellite Photogrammetry: Involves using satellite images to create 3D models and maps.
  Used for large-scale mapping, environmental monitoring, disaster management, and military intelligence.
  Covers large areas, useful for remote or inaccessible regions, lower resolution compared to aerial photogrammetry.

## Slide 7: Applications
Topographic Mapping: Creating detailed and accurate maps of the Earth's surface such as:
  Designing and planning urban infrastructure.
  Road construction, bridge building, and other infrastructure projects.
  Monitoring landscape changes, erosion, and natural disasters.
Architecture and Heritage Conservation: Documenting and preserving historical and architectural sites such as:
  Creating detailed 3D models of buildings and structures.

## Slide 8: Applications
  Assisting in the accurate restoration of historical sites.
  Digitally preserving monuments and artifacts.
Forensics and Accident Investigation: Analyzing crime scenes and accidents such as:
  Creating accurate 3D models of crime scenes for analysis and courtroom presentations.
  Documenting and reconstructing accident scenes to determine causes and responsibilities.
  Capturing detailed and precise records of evidence.

## Slide 9: Applications
Environmental Monitoring and Management: Tracking and managing environmental changes such as:
  Monitoring deforestation, urban planning, and agricultural development.
  Assessing damage from natural disasters such as floods, earthquakes, and hurricanes.
  Tracking wildlife habitats, forest health, and ecosystem changes.

## Slide 10: Applications
Agriculture and Forestry: Enhancing productivity and managing natural resources such as:
  Monitoring crop health, soil conditions, and irrigation needs.
  Mapping forest areas, tracking deforestation, and managing timber resources.
  Assessing land suitability for different agricultural uses.
Medicine and Healthcare: Improving diagnostics and treatment planning such as:
  Creating 3D models of organs and tissues for diagnosis and surgery planning.
  Analyzing injuries and determining causes of death.

## Slide 11: Applications
Autonomous Vehicles and Robotics: Enhancing navigation and environmental interaction such as:
  Providing accurate 3D maps for autonomous vehicle navigation.
  Enabling robots to interact with their environment through detailed 3D models.
  Enhancing obstacle detection and avoidance.

## Slide 12: Orientation and Triangulation
Orientation: The process of determining the position and orientation of the camera when the photograph was taken.
Steps in Orientation:
Interior Orientation: Determining the internal geometry of the camera or sensor at the time of image capture such as focal length, principal point, and lens distortions.
Exterior Orientation: Determining the position (X, Y, Z coordinates) and orientation (angles of rotation) of the camera in space at the time of image capture.

## Slide 13: Orientation and Triangulation
Triangulation: Uses multiple photographs to determine the 3D coordinates of points on an object.
This requires at least two images taken from different perspectives, with overlapping fields of view.
Triangulation Process:
Identify common points in multiple images.
Calculating the angles between the lines of sight from the camera positions to the points.
Use geometric principles to calculate 3D coordinates.

## Slide 14: Orientation and Triangulation
Steps in Triangulation:
  Image Acquisition: Capture overlapping images from different angles.
  Point Identification: Identify common points in different images.
  Bundle Adjustment: Simultaneous adjustment of image points and camera parameters to minimize discrepancies.
  3D Point Calculation: Use triangulation algorithms to calculate the 3D coordinates of points.

## Slide 15: Stereo Model Compilation
The process of creating a 3D model from a pair of overlapping photographs taken from different viewpoints.
This process includes identifying corresponding points in the two images, which are then used to calculate the depth information.
The results in a stereoscopic model that can be used for various applications, such as topographic mapping or 3D object modeling.

## Slide 16: Stereo Model Compilation
Tools and Software:
  Photogrammetry software (e.g., Agisoft Metashape, Pix4D)
  Digital stereo plotters
Challenges:
Requires high-quality, high-resolution images to ensure accurate results.
Needs sufficient overlap between images to identify common points and ensure complete coverage of the area.

## Slide 17: Stereo Model Compilation: Challenges
Weather conditions, lighting, and shadows can affect image quality and the resulting model.
Processing large numbers of high-resolution images can be computationally intensive and time-consuming.

## Slide 18: Stereoscopic 3D Viewing
This is a technique of used to visualize and analyze 3D models generated from photogrammetry.
This is a viewing technique that involves using two overlapping images to create perception of depth and allow viewers to see 3D structure.
Stereoscopic Viewing Process:
  Image Capture: Take two overlapping images of the same scene from different angles.
  Alignment: Align the images to ensure proper overlap and orientation.

## Slide 19: Stereoscopic 3D Viewing: Process
  Viewing: Use a stereoscope or digital 3D viewing setup to see the images. The brain combines the two images to perceive depth.
  Challenges:
    Requires specialized viewing equipment.
    High-quality images are necessary.
    Users need to be trained to interpret stereoscopic images correctly

## Slide 20: Stereoscopic 3D Viewing
Tools Used:
  Stereoscope: A device for viewing a stereoscopic pair of separate images.
  3D Glasses: Glasses with lenses that filter images to each eye to create a 3D effect.
Applications:
  Enhanced visualization in medical imaging, remote sensing, and virtual reality.

## Slide 21: Stereoscopic Measurement
The technique used to measure distances and create 3D models by analyzing the parallax (the apparent shift in position) between two images taken from slightly different viewpoints.
This includes measuring distances, angles, areas, and volumes.
Useful in various fields such as architecture, engineering, archaeology, and forensic science, where accurate spatial data is necessary.

## Slide 22: Stereoscopic Measurement
Techniques:
Parallax Measurement: Measuring the apparent shift in position of an object when viewed from different angles.
Coordinate Measurement: Using the known geometry of the stereo model to calculate distances.

## Slide 23: Stereoscopic Measurement
Advantages:
  High accuracy and precision.
  Ability to measure inaccessible or hazardous areas.
  Applicable to a wide range of fields from geography and engineering to archaeology and forensics.
Limitations:
  Requires skilled personnel.
  Requires clear and overlapping images.
  Sensitive to environmental conditions (e.g., lighting, weather).
  Computationally intensive processing.

## Slide 24: Conclusion
Photogrammetry combines principles of geometry, optics, and mathematics to extract 3D information from photographs.
It is a versatile and powerful tool for mapping, modeling, and measuring.
Photogrammetry involves complex processes of orientation, triangulation, stereo model compilation, and stereoscopic viewing.
It has diverse applications in various fields, offering precise measurements and 3D visualization.
Its applications range from urban planning and heritage conservation to environmental monitoring and autonomous vehicles.

## Slide 25: References
Books:
"Photogrammetry: Geometry from Images and Laser Scans" by Karl Kraus
"Introduction to Modern Photogrammetry" by Edward M. Mikhail, James S. Bethel, J. Chris McGlone

## Slide 26
Thank You